## Slide 1
Constrained of Application Protocol

## Slide 2: CoAP Content
CoAP Overview
CoAP Methods
CoAP Message format
CoAP Workflow

## Slide 3
CoAP Overview
What is CoAP?
Internet Application Protocol for constrained devices
Work on Constrained RESTful Environments
Protocol for Embedded devices, IoT, M2M
Easily translates to HTTP for intergration

## Slide 4
CoAP Overview
CoAP features
Web protocol fulfilling M2M requirements in constrained environments
UDP binding with optional reliability supporting unicast and multicast requests.
Asynchronous message exchanges.
Low header overhead and parsing complexity.
URI and Content-type support.
Simple proxy and caching capabilities.
A stateless HTTP mapping, allowing proxies to be built providing access to CoAP resources via HTTP in a uniform way or for HTTP simple interfaces to be realized alternatively over CoAP.
Security binding to Datagram Transport Layer Security (DTLS)

## Slide 5
CoAP Overview
CoAP advantages
CoAP is Lightweight:
- Message is simple binary format (4 bytes header) -> easy to parse, space efficient.
- Client and server share the internal structures, so easy to implement both client and server compare to HTTP.
CoAP is faster than HTTP
- Implement on top of UDP (Broadcast and Multicast), fast but unreliable.
- Stateless, no connection, less overhead.
- Omite the protocol level reliability.
CoAP is almost like HTTP
- Request and Response model.
- RESTfull design, GET/PUT/POST/DELETE method.
- Addressable by URL with query string
- Content-Type can be specified, but limited to pre-defined types, text, json, xml, etc…

## Slide 6
CoAP Methods
GET Method
The GET method retrieves a representation for the information that currently corresponds to the resource identified by the request URI.
If the request includes an Accept Option, that indicates the preferred content-format of a response.
We can only send limited data with GET method and it’s sent in the header request URL whereas
We can send large amount of data with POST because it’s part of the request body.

## Slide 7
CoAP Methods
GET Method
Confirmable Message
Some messages require an acknowledgement. These messages are called “Confirmable“;
When no packets are lost, each Confirmable message elicits exactly one return message of type Acknowledgement or type Reset.

## Slide 8
CoAP Methods
GET Method
The Token Option
  is an opaque sequence of 1-2 bytes
  which is used to match a request with a response
  is meant for use with asynchronous responses by this specification.
  the Token is generated by a client and included in a way that Token values currently in use are unique.

## Slide 9
CoAP Methods
POST Method
The POST method is used to request the server to create a new subordinate resource under the requested parent URI.
If a resource has been created on the server, the response SHOULD be 201 (Created) including the URI of the new resource in a Location Option with any possible status in the message body.
If the POST succeeds but does not result in a new resource being created on the server, a 200 (OK) response code SHOULD be returned.
Server
Client
CON [ox1c] POST/ light Token: 0x33
ACK [ox1c] POST/ 201 Create
58.2; Token: 0x33
POST can transfer data securely to server, it can transfer large data and should be used to send data to server;

## Slide 10
CoAP Methods
History | Parameters remain in browser history because they are part of the URL | Parameters are not saved in browser history.
Bookmarked | Can be bookmarked. | Cannot be bookmarked.
BACK button/re-submit behaviour | GET requests are re-executed but may not be re-submitted to server if the HTML is stored in the browser cache. | The browser usually alerts the user that data will need to be re-submitted.
Encoding type (ectype attribute) | application/x-www-form-urlencoded | multipart/form-data or application/x-www-form-urlencoded Use multipart encoding for binary data.
Parameters | can send but the parameter data is limited to what we can stuff into the request line (URL). Safest to use less than 2K of parameters, some servers handle up to 64K | Can send parameters, including uploading files, to the server.
Hacked | Easier to hack for script kiddies | More difficult to hack
Restrictions on form data type | Yes, only ASCII characters allowed. | No restrictions. Binary data is also allowed.
Security | GET is less secure compared to POST because data sent is part of the URL. So it's saved in browser history and server logs in plaintext. | POST is a little safer than GET because the parameters are not stored in browser history or in web server logs.
Restrictions on form data length | Yes, since form data is in the URL and URL length is restricted. A safe URL length limit is often 2048 characters but varies by browser and web server. | No restrictions
Usability | GET method should not be used when sending passwords or other sensitive information. | POST method used when sending passwords or other sensitive information.
Visibility | GET method is visible to everyone (it will be displayed in the browser's address bar) and has limits on the amount of information to send. | POST method variables are not displayed in the URL.
Cached | Can be cached | Not cached
GET
POST

## Slide 11
CoAP Methods
PUT Method
The PUT method requests that the resource identified by the request URI be updated or created with the enclosed message body.
If a resource exists at that URI the message body SHOULD be considered a modified version of that resource, and a 200 (OK) response SHOULD be returned.
If no resource exists then the server MAY create a new resource with that URI, resulting in a 201 (Created) response.
If the resource could not be created or modified, then an appropriate error response code SHOULD be sent. Responses to this method are not cacheable.
PUT:- Used when the client is sending a replacement document or uploading a new document to the Web server under the request URL

## Slide 12
CoAP Methods
DELETE Method
The DELETE method requests that the resource identified by the request URI be deleted.
The response 200 (OK) SHOULD be sent on success.
Responses to this method are not cacheable.
DELETE:- Used when the client is trying to delete a document from the Web server, identified by the request URL.

## Slide 13
CoAP Message Format
CoAP messages are encoded in a simple binary format.
The Message Header (4 bytes).
The variable-length token value 0 and 8 bytes long.
Ver - Version (1)  2 bit unsigned integer . Implementations of this field to 1 (01 binary).
T – Message Type  2- bit unsigned integer. (Confirmable, Non-Confirmable, Acknowledgement, Reset).
TKL- Token Length  4-bit unsigned integer. Indicates the length of the variable-length Token field (0-8 bytes).
Code – 8-bit unsighted integer. 3 bit class(most signification bits). 5 bits detail (least significant bits).
Request Method (1-10) or Response Code (40-255)
Message ID – 16-bit identifier for matching responses
Token – Optional response matching token

## Slide 14
CoAP Message Format
CoAP defined a number of options that can be included in a message.
Option Delta - Difference between this option type and the previous.
4 bit unsigned integer. A value between 0 and 12 indicates the Optional Delta.
Length - Length of the option value
4 bit unsigned integer. A value between 0 and 12 indicates the length of the Optional Value, in bytes.
Value - The value of Length bytes immediately follows Length

## Slide 15
CoAP Workflow

## Slide 16
Thank You !