## Slide 1: Device Management with OMA Lightweight M2M
Simon Lemay and Hannes Tschofenig

## Slide 2: Overview
Why Lightweight Device Management
OMA Lightweight M2M Standard
Bootstrapping Interface
Object Model
Access Control Model
Application Server Interaction
Example Flows
©Sensinode 2013

## Slide 3: Why Lightweight Device Management

## Slide 4: Why Lightweight Device Management?
Traditional Device Management (DM) is widely used in mobile devices
  Used by operators and enterprises for managing smart phones, tablets and laptops
  Some M2M DM use today with cellular devices, mostly proprietary
  OMA DM was one of the first standards for device management in the mobile handset sector.
  In the meanwhile various standards exist that provide similar functionality, such as TR 69, or IEEE 802.1AR.
OMA Lightweight M2M (LWM2M) created to serve the IoT market with a focus on lightweight nature:
  Applicable to various radio technologies (devices just need IP connectivity)
  Extensible object model and registry open to the whole industry
  Enables both management and application data handling with the same solution
  Addresses security need for software updates and device re-configuration.
  Re-uses IETF specifications.

## Slide 5: Features
Mobile Device Management
Device Management
Bootstrapping
Device Configuration
Firmware Update
Fault Management
Key management
Service provisioning
Access Control
Changes to settings
Changes to parameters of the device
Update application and system software
Bug fixes
Report Errors from devices
Query about status of devices
Application
Configuration & Control
Reporting
Configure settings of the application
Send control commands
Notify changes in sensor values
Notify alarms and events

## Slide 6: OMA LWM2M Architecture
M2M Applications
  Application abstraction through REST API
  Resource Discovery and Linking
LWM2M Clients are Devices
  Device abstraction through CoAP
  LWM2M Clients are CoAP Servers
  Any IP network connection
LWM2M Server
  Reuses IETF technologies, such as the CoAP protocol, DTLS, Resource Directory.
  Deployable on gateways and in the cloud

## Slide 7: LWM2M Interfaces
Bootstrap Interface
  Configure Servers & Keys & ACLs
  Pre-Configured, Smart Card, or Server Initiated Bootstrap
  CoAP REST API
Registration Interface
  RFC 6690 and Resource Directory
Management Interface Using Objects
  Management Objects and Resources
  CoAP REST API
Reporting Interface
  Object Instances and Resources Report
  Asynchronous notification using CoAP Observe

## Slide 8: Bootstrap Interface

## Slide 9: Bootstrapping Architecture

## Slide 10: Bootstrapping
©Sensinode 2013

## Slide 12: Bootstrapping Features
OMA LWM2M supports different credential provisioning procedures:
  Pre-shared Secrets
  Raw Public Keys
  Certificates
These credentials are provisioned by the Bootstrap Server for use with LWM2M servers.
It is possible to mix credentials for use with different servers and even to use different credentials in a single client/server interaction.
The LWM2M client is assumed to possess credentials for authentication to the Bootstrap Server. These credentials are typically pre-provisioned during manufacturing time.

## Slide 13: Pre-Shared Key Mode

## Slide 14: Raw Public Key Mode

## Slide 15: Certificate Mode

## Slide 16: A few more details
  LWM2M Client may be pre-provisioned with information about the LWM2M Server (rather than distributing credentials with the bootstrapping protocol)
  LWM2M Client MUST have a LWM2M Bootstrap Server Account (+Bootstrap Server URI, Endpoint Client Name)
  LWM2M Security Object
          Security Mode (PSK, raw public key, certificate, no-sec)
          Public Key or Identity (certificate, public key, or PSK identity)
          Server Public Key or Identity (LWM2M server or bootstrap server certificate, public key or PSK identity)
          Secret Key (secret key or private key)
          LWM2M Server URI (bootstrap server or LWM2M server)
          Bootstrap Server (true – false)

## Slide 17: Object Model

## Slide 18: Object Model
A LWM2M Client has one or more Object Instances
An Object is a collection of Resources
A Resource is an atomic piece of information that can be
  Read, Written or Executed
Resources can have multiple instances
Access control list (ACL) objects control access to objects accessed by LWM2M Servers
Objects and Resources are identified by a 16-bit Integer, Instances by an 8-bit Integer
Objects/Resources are accessed with simple URIs:
/{Object ID}/{Object Instance}/{Resource ID}
Example: /3/0/1 = 3 = Device Object, 0 = Object Instance #0, 1 = Manufacturer Resource
©Sensinode 2013

## Slide 19: Standard Device Management Objects
The LWM2M Technical Specification defines eight normative Objects
Object Name | ID | Multiple Instances? | Description
LWM2M Security | 0 | Yes | This LWM2M Object provides the keying material of a LWM2M Client appropriate to access a specified LWM2M Server.
LWM2M Server | 1 | Yes | This LWM2M objects provides the data related to a LWM2M server.
Access Control | 2 | Yes | Access Control Object is used to check whether the LWM2M Server has access right for performing an operation.
Device | 3 | No | This LWM2M Object provides a range of device related information which can be queried by the LWM2M Server, and a device reboot and factory reset function.
Connectivity Monitoring | 4 | No | This LWM2M objects enables monitoring of parameters related to network connectivity.
Firmware | 5 | No | This Object includes installing firmware package, updating firmware, and performing actions after updating firmware.
Location | 6 | No | The GPS location of the device.
Connectivity Statistics | 7 | No | This LWM2M Objects enables client to collect statistical information and enables the LWM2M Server to retrieve these information, set the collection duration and reset the statistical parameters.

## Slide 20: Object Example
Example of the LWM2M Location Object, which has 6 Resources

## Slide 21: Defining new Objects
Defining a new Object is straightforward
Object IDs are registered with the OMA Naming Authority (OMNA)
Who can register an Object?
    OMA working groups
    3rd party organizations
    Enterprises
How to register an Object?
  Write a specification filling out the Object template tables:
    Object Name, Description and if it can have Multiple Instances
    The list of resources the Object defines
  Fill out the Lightweight Object form on-line.
IPSO Alliance has created additional objects, which are documented here (Starter Pack) and here (Expansion Pack).

## Slide 22: Access Control Model

## Slide 23: Overview
Bootstrap servers distribute access control lists to LWM2M clients.
Example from Appendix F of the OMA LWM2M technical specification: (Table shows example objects provisioned at a LWM2M client by the Bootstrap server.)

## Slide 24: Overview, cont.
LWM2M
Client
LWM2M
Server 2
Luminaire
LWM2M
Client 3
Registration and resource access
Light Switch
ACL: <Server 1, RW>
LWM2M
Server 1
Registration and resource access
LWM2M
Bootstrap Server
Application
ACL: <Server 2, RW>

## Slide 25: Discussion
ACLs work well when a Bootstrap Server is aware of the future interactions between LWM2M servers and LWM2M clients.
Real-time provisioning of ACLs by the Bootstrap Server is also possible.
During registration a LWM2M client is a CoAP client; afterwards it becomes a CoAP server waiting for incoming CoAP requests.
Notes:
  LWM2M clients can become LWM2M servers in another communication setup and may therefore also receive ACLs from the Bootstrap Server. In our example light switches and luminaires are LWM2M clients in different communication scenarios.
  Different LWM2M clients may also use different Bootstrap Servers.
  A single LWM2M client may also have more than one Bootstrap Server (e.g., for redundancy/ purpose)

## Slide 26: Application Server Interaction

## Slide 27: LWM2M Application Server
Web Server App
LWM2M Server
Soft Endpoints
IP Device
IP Device
LWM2M Clients
DISCOVER
REGISTER
/3303/0/5700
/domain/endpoints/3303/0/5700

## Slide 28: LWM2M Application Server
Web Server App
LWM2M Server
IP Device
IP Device
LWM2M Clients
1. GET
3. REPLY
2. GET
4. REPLY
/domain/endpoints/3303/0/5700
/3303/0/5700

## Slide 29: LWM2M Application Server
Web Server App
LWM2M Server
IP Device
IP Device
LWM2M Clients
1. NOTIFY
2. NOTIFY

## Slide 30: LWM2M Supports Sleeping Endpoints “b=uq”
Client uses the registration refresh to inform LWM2M server that it is awake, and listens for any queued operations

## Slide 31: Observe Parameters
LWM2M provides a mechanism to control Observation
“Write Attributes” Interface using query parameters to set observe attributes:
Pmin – minimum observation quiet period, to limit notification frequency
Pmax – maximum observation quiet period, to guarantee notifications
Lt – low limit measurement notification, like low alarm, in engineering units
Gt – high limit measurement notification, like a high alarm, in engineering units
Step – Minimum delta change required to notify, in engineering units

## Slide 32: LWM2M Bulk Read
Returns TLV or JSON based on requested content-format
CBOR needs to be added
Linked Objects are supported
{“e”:[
{"n":"0","sv":"Open Mobile Alliance"},
{"n":"1","sv":"Lightweight M2M Client"},
{"n":"2","sv":"345000123"},
{"n":"3","sv":"1.0"},
{"n":"6/0","v":"1"},
{"n":"6/1","v":"5"},
{"n":"7/0","v":"3800"},
{"n":"7/1","v":"5000"},
{"n":"8/0","v":"125"},
{"n":"8/1","v":"900"},
{"n":"9","v":"100"},
{"n":"10","v":"15"},
{"n":"11/0","v":"0"},
{"n":"13","v":"1367491215"},
{"n":"14","sv":"+02:00"},
{"n":"15","sv":"U"}]
}

## Slide 33: LWM2M Uses CoRE RD Resource Links (RFC 6690)
Links are uploaded during registration to inform the LWM2M server about resources on the endpoint
Links are discovered using GET with content type “application/link-format”
JSON representation using content type “application/link-format+json”
<4001/0/9002>;rt=“oma.lwm2m”;ct=50;obs=1
Resource Type
Content Type
Observable

## Slide 34: Example Flows

## Slide 35: Interface Flows
©Sensinode 2013

## Slide 36: Registration
©Sensinode 2013

## Slide 37: Object Access
©Sensinode 2013

## Slide 38: Notification
©Sensinode 2013

## Slide 39: Queue Mode (Sleeping Devices)
©Sensinode 2013

## Slide 40: Summary
LWM2M re-uses many IETF specifications. Specifications are publically available for download here.
Implementations and products are available. Example: Leshan (as an open source implementation)
Several plugfests took place already and there the issue list can be found here.
Work on a bugfix release is in progress and the Version 1.1 specification work will be started soon to specification with ongoing IETF work.

## Slide 41: Using LWM2M with ARM
Create your application with mbed Client. Examples:
mbed client (Linux)
mbed client (mbed OS)
Connect your IoT devices to the mbed Device Connector at https://connector.mbed.com
Create your web application with example code or REST API
Links:
Example code
Documentation